## Slide 1: Boolean Algebra
Developed by English Mathematician George Boole in between 1815 - 1864.
It is described as an algebra of logic or an algebra of two values i.e True or False.
The term logic means a statement having binary decisions i.e True/Yes or False/No.

## Slide 2: APPLICATION OF BOOLEAN ALGEBRA
It is used to perform the logical operations in digital computer.
In digital computer True represent by ‘1’ (high volt) and False represent by ‘0’ (low volt)
Logical operations are performed by logical operators. The fundamental logical operators are:
1. AND (conjunction)
2. OR (disjunction)
3. NOT (negation/complement)

## Slide 3: AND operator
It performs logical multiplication and denoted by (.) dot.
X Y X.Y
0 0 0
0 1 0
1 0 0
1 1 1

## Slide 4: OR operator
It performs logical addition and denoted by (+) plus.
X Y X+Y
0 0 0
0 1 1
1 0 1
1 1 1

## Slide 5: NOT operator
It performs logical negation and denoted by (-) bar. It operates on single variable.
X X (means complement of x)
0 1
1 0

## Slide 6: Truth Table
Truth table is a table that contains all possible values of logical variables/statements in a Boolean expression.
No. of possible combination =
2n, where n=number of variables used in a Boolean expression.

## Slide 7: Truth Table
The truth table for XY + Z is as follows:
Dec X Y Z XY XY+Z
0 0 0 0 0 0
1 0 0 1 0 1
2 0 1 0 0 0
3 0 1 1 0 1
4 1 0 0 0 0
5 1 0 1 0 1
6 1 1 0 1 1
7 1 1 1 1 1

## Slide 8: Tautology & Fallacy
If the output of Boolean expression is always True or 1 is called Tautology.
If the output of Boolean expression is always False or 0 is called Fallacy.

## Slide 9: Exercise
1. Evaluate the following Boolean expression using Truth Table.
(a) X’Y’+X’Y (b) X’YZ’+XY’
(c) XY’(Z+YZ’)+Z’
2. Verify that P+(PQ)’ is a Tautology.
3. Verify that (X+Y)’=X’Y’

## Slide 10: Implementation
Boolean Algebra applied in computers electronic circuits. These circuits perform Boolean operations and these are called logic circuits or logic gates.

## Slide 11: Logic Gate
A gate is an digital circuit which operates on one or more signals and produce single output.
Gates are digital circuits because the input and output signals are denoted by either 1(high voltage) or 0(low voltage).
There are three basic gates and are:
1. AND gate
2. OR gate
3. NOT gate

## Slide 12: AND gate
The AND gate is an electronic circuit that gives a high output (1) only if all its inputs are high.
AND gate takes two or more input signals and produce only one output signal.
Input A | Input B | Output AB
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 13: OR gate
The OR gate is an electronic circuit that gives a high output (1) if one or more of its inputs are high.
OR gate also takes two or more input signals and produce only one output signal.
Input A | Input B | Output A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 14: NOT gate
The NOT gate is an electronic circuit that gives a high output (1) if its input is low .
NOT gate takes only one input signal and produce only one output signal.
The output of NOT gate is complement of its input.
It is also called inverter.
Input A | Output A
0 | 1
1 | 0

## Slide 15
AND Gate
So while going out of the house you set the "Alarm Switch" and if the burglar enters he will set the "Person switch", and tada the alarm will ring.
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 16
AND Gate
PRACTICAL APPLICATIONS OF LOGIC GATES
Electronic door will only open if it detects a person and the switch is set to unlocked.
Microwave will only start if the start button is pressed and the door close switch is closed.

## Slide 17
OR Gate
You would of course want your doorbell to ring when someone presses either the front door switch or the back door switch.
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 18
NOT Gate
When the temperature falls below 20c the Not gate will set on the central heating system (cool huh).
PRACTICAL APPLICATIONS OF LOGIC GATES

## Slide 19
NAND Gate
Known as a “universal” gate because ANY digital circuit can be implemented with NAND gates alone.

## Slide 20
NAND Gate
NAND
X
Y
Z
X Y Z
0 0 1
0 1 1
1 0 1
1 1 0
Z = ~(X & Y)
nand(Z,X,Y)

## Slide 21
NAND Gate
X
X
F = (X•X)’
= X’+X’
= X’
X
Y
Y
F = ((X•Y)’)’
= (X’+Y’)’
= X’’•Y’’
= X•Y
F = (X’•Y’)’
= X’’+Y’’
= X+Y
X
X
F = X’
X
Y
Y
F X•Y
F = X+Y

## Slide 22
NOR Gate
NOR
X
Y
Z
X Y Z
0 0 1
0 1 0
1 0 0
1 1 0
Z = ~(X | Y)
nor(Z,X,Y)

## Slide 23
Exclusive-OR Gate
X Y Z
XOR
X
Y
Z
0 0 0
0 1 1
1 0 1
1 1 0
Z = X ^ Y
xor(Z,X,Y)

## Slide 24
Exclusive-NOR Gate
X Y Z
XNOR
X
Y
Z
0 0 1
0 1 0
1 0 0
1 1 1
Z = ~(X ^ Y)
Z = X ~^ Y
xnor(Z,X,Y)

## Slide 25: Basic Theorem of Boolean Algebra
T1 : Properties of 0
  (a) 0 + A = A (b) 0 A = 0
T2 : Properties of 1
  (a) 1 + A = 1 (b) 1 A = A

## Slide 26: Basic Theorem of Boolean Algebra
T3 : Commutative Law
  (a) A + B = B + A (b) A B = B A
T4 : Associate Law
  (a) (A + B) + C = A + (B + C) (b) (A B) C = A (B C)
T5 : Distributive Law
  (a) A (B + C) = A B + A C (b) A + (B C) = (A + B) (A + C)
  (c) A+A’B = A+B

## Slide 27: Basic Theorem of Boolean Algebra
T6 : Indempotence (Identity ) Law
  (a) A + A = A (b) A A = A
T7 : Absorption (Redundance) Law
  (a) A + A B = A (b) A (A + B) = A

## Slide 28: Basic Theorem of Boolean Algebra
T8 : Complementary Law
  (a) X+X’=1
  (b) X.X’=0
T9 : Involution
  (a) x’’ = x
T10 : De Morgan's Theorem
  (a) (X+Y)’=X’.Y’
  (b) (X.Y)’=X’+Y’

## Slide 29: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 30: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 31: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 32: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 33: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 34: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 35
Simplify:
A.(A + B) =A
AB(BC + AC)
(A + B + C)(A +B + C)(A + B + C)
(A + B)(A + C)

## Slide 37
A.(A + B) =A
(A + B)(A + C) = A + B.C
AB(BC+AC) = ABC
(A + B + C)(A +B + C)(A + B + C= A + (B C)

## Slide 38: K-Map
Steps to Solve Expression using K-map
Select the K-map according to the number of variables.
Identify minterms or maxterms as given in the problem.
For SOP put 1’s in blocks of K-map respective to the minterms (0’s elsewhere).
For POS put 0’s in blocks of K-map respective to the max terms (1’s elsewhere).
Make rectangular groups containing total terms in power of two like 2,4,8 ..(except 1) and try to cover as many elements as you can in one group.
From the groups made in step 5 find the product terms and sum them up for SOP form.

## Slide 40
(A' + B’) (B’ + C’) (A + B + C)

## Slide 42
(C+D’+B’).(C’+D’+A).(A’+C+D).(A’+B+C’)

## Slide 47
The DEMUX is a digital information processor. It takes input from one source and also converts the data to transmit towards various sources. The demultiplexer has one data input line. The demultiplexer has several control lines (also known as select lines). These lines determine to which output the input data should be sent. The number of control lines determines the number of output lines.

## Slide 48: Difference between MUX and DeMUX

## Slide 50
Applications of MUX
MUX i.e., multiplexer has many applications in different fields. Some of these applications are listed below.
Implementation of Digital Circuits
Control Unit of CPU
Parallel to Serial Data Conversion
Computer Memory
Data Routing
Communication Systems

## Slide 51
Applications of DEMUX
DEMUXs are majorly used to design the ALU circuits and parallel data segments.
The DEMUXs convert the output of the MUX into the actual input. On the receiver end, the DEMUX can be used to verify the original form of the data to carry out the entire communication process.
DEMUX helps to save the output. The output generally saved to the ALU. The output will be saved in the registers and the various storage units of the system.
Each DEMUX has a connection with multiple registers which helps to store the processed data into it.
The counterpart of the DEMUX regulates the data signal at the output stage of the DEMUX operation. These data can be retrieved later to read out parallelly.
In the audio or video system, the DEMUX distributes them in different channels. In broadcasting, the DEMUX separates the composite signal into an individual one.

## Slide 52
Binary code of N digits can be used to store 2N distinct elements of coded information. This is what encoders and decoders are used for.
Encoders convert 2N lines of input into a code of N bits and Decoders decode the N bits into 2N lines.
Encoders – An encoder is a combinational circuit that converts binary information in the form of a 2N input lines into N output lines, which represent N bit code for the input. For simple encoders, it is assumed that only one input line is active at a time. As an example, let’s consider Octal to Binary encoder. As shown in the following figure, an octal-to-binary encoder takes 8 input lines and generates 3 output lines.

## Slide 53
From the truth table, the output line Z is active when the input octal digit is 1, 3, 5 or 7. Similarly, Y is 1 when input octal digit is 2, 3, 6 or 7 and X is 1 for input octal digits 4, 5, 6 or 7. Hence, the Boolean functions would be:
X = D4 + D5 + D6 + D7 Y = D2 +D3 + D6 + D7 Z = D1 + D3 + D5 + D7

## Slide 55
4 to 1 MUX
library ieee;
use ieee.std_logic_1164.all;
entity mux_4to1 is
port( A,B,C,D : in bit;
S1,S0: in bit;
Y: out bit);
end mux_4to1;
architecture bhv of mux_4to1 is
begin
process (A,B,C,D,S0,S1) is
begin
if (S1 ='0' and S0 = '0') then
Y<= A;
elsif (S1 ='0' and S0 = '1') then
Y<= B;
elsif (S1 ='1' and S0 = '0') then
Y<= C;
else
Y<= D;
end if;
end process;
end bhv;

## Slide 56
A decoder does the opposite job of an encoder. It is a combinational circuit that converts n lines of input into 2n lines of output.
Example of 3-to-8 line decoder.
D0 = X’ Y’ Z’
D1 = X’ Y’ Z
D2 = X’ Y Z’
D3 = X’ Y Z
D4 = X Y’ Z’
D5 = X Y’ Z
D6 = X Y Z’
D7 = X Y Z

## Slide 61
Binary to BCD code converter
In BCD code, 0 to 9 numbers represent the equivalent binary numbers. For the numbers above 10, LSB of a decimal number is represented by its equivalent binary number and MSB of a decimal number is also represented by their equivalent binary numbers.

## Slide 62
The truth table shows the conversion between the binary code input and the BCD code output. As you see from the table, the 4-bit binary number is converted into 5-bit BCD code. Decimal code is added in the table to understand the equivalence of Binary and BCD code

## Slide 63
D4 = ∑m(10, 11, 12, 13, 14, 15), D3 = ∑m(8, 9), D2 = ∑m(4, 5, 6, 7, 14, 15), D1 = ∑m(2, 3, 6, 7, 12, 13), D0 = ∑m(1, 3, 5, 7, 9, 11, 13, 15)

## Slide 65
Code Converters are the digital circuits or algorithms that are designed to translate data representation from one format to the other format. In this article, we will go through binary to gray code converters.
binary-to-Gray code converter takes binary input and translates it to its corresponding gray code representation
What is a Gray Code?
Gray Code system is a binary number system in which every successive pair of numbers differs by only one bit It is also known as
Unity Hamming Distance Code
Cyclic Code
Reflecting Code

## Slide 67
Binary to Gray conversion :
The Most Significant Bit (MSB) of the gray code is always equal to the MSB of the given binary code.
Other bits of the output gray code can be obtained by XORing binary code bit at that index and previous index.

## Slide 68
Gray to binary conversion :
The Most Significant Bit (MSB) of the binary code is always equal to the MSB of the given gray code.
Other bits of the output binary code can be obtained by checking the gray code bit at that index. If the current gray code bit is 0, then copy the previous binary code bit, else copy the invert of the previous binary code bit.

## Slide 70
1 to 4 DEMUX
library ieee;
use ieee.std_logic_1164.all;
entity demux_1to4 is
port(F : in bit;
S0,S1: in bit;
A,B,C,D: out bit);
end demux_1to4;
architecture bhv of demux_1to4 is
begin
process (F,S0,S1) is
begin
if (S1 ='0' and S0 = '0') then
A <= F;
elsif (S1 ='0' and S0 = '1') then
B <= F;
elsif (S1 ='1' and S1 = '0') then
C <= F;
else
D <= F;
end if;
end process;
end bhv;